## Slide 1
RASPBERRY PI / BUILD GUIDE
Smart obstacle
alert glasses
Setup, wiring, software, and automatic startup
Distance alerts • Button-triggered camera scan • Spoken description
RASPBERRY PI
CPU
POWER
SENSOR
MOTOR
A visual walkthrough for a first boot-to-running setup.
01

## Slide 2
SMART OBSTACLE GLASSES / SETUP
System overview
RASPBERRY PI BUILD GUIDE • 02
01
Measure
Ultrasonic sensor checks the space ahead repeatedly.
02
Alert
Pulses get closer together as an obstacle gets nearer.
03
Describe
Press the button for a photo and short spoken description.
04
Start
A system service launches the program after boot.
The distance monitor and button-controlled camera scan operate independently.

## Slide 3
SMART OBSTACLE GLASSES / SETUP
GPIO pin map
RASPBERRY PI BUILD GUIDE • 03
The script uses BCM pin numbers. Match signal names, not physical header positions.
GPIO 4
Button signal
GPIO 26
Vibration output
GPIO 27
Ultrasonic TRIG
GPIO 22
Ultrasonic ECHO
3V3 + GND
Sensor power / shared ground
Pi header (diagram only)
GPIO 26
GPIO 27 / 22
Confirm each BCM pin against your Pi model’s pinout before connecting wires.

## Slide 4
SMART OBSTACLE GLASSES / SETUP
Ultrasonic sensor wiring
RASPBERRY PI BUILD GUIDE • 04
HC-SR04-style sensor
VCC
3V3 (your current wiring)
GND
Pi ground
TRIG
GPIO 27
ECHO
GPIO 22
HC-SR04
VCC
TRIG
ECHO
GND
Voltage check
Sensor versions differ. Check its label or datasheet: some require 5 V. If ECHO can reach 5 V, use a divider or level shifter before Pi GPIO 22.
If powered from Pi 3V3 and readings work, keep the tested setup for now; confirm the exact module rating.
Notes: Raspberry Pi GPIO uses 3.3 V logic. Verify the exact ultrasonic module voltage and output level before connecting ECHO.

## Slide 5
SMART OBSTACLE GLASSES / SETUP
Vibration motor connection
RASPBERRY PI BUILD GUIDE • 05
The prepared script pulses GPIO 26. Your tested direct connection is enabled.
Pi GPIO 26
signal
Motor driver
transistor / MOSFET
Vibration motor
motor supply
Recommended upgrade
A motor driver takes the motor current while GPIO 26 provides only the control signal. Use a suitable driver circuit and shared ground.
Direct GPIO-to-motor wiring may damage the Pi over time, even if it has worked in your test.

## Slide 6
SMART OBSTACLE GLASSES / SETUP
Install files and dependencies
RASPBERRY PI BUILD GUIDE • 06
1
Create folder
mkdir -p ~/obstacle-glasses
2
Copy script
Place test1.py in ~/obstacle-glasses/
3
Install system tools
sudo apt update
sudo apt install python3-venv python3-full python3-rpi.gpio fswebcam mpg123
4
Create a venv
cd ~/obstacle-glasses
python3 -m venv --system-site-packages .venv
.venv/bin/pip install openai gTTS
Raspberry Pi OS Bookworm and later require pip packages to be installed in a virtual environment.
Notes: Raspberry Pi documentation: https://www.raspberrypi.com/documentation/usage/gpio/python/

## Slide 7
SMART OBSTACLE GLASSES / SETUP
API key setup
RASPBERRY PI BUILD GUIDE • 07
The script reads the key from OPENAI_API_KEY.
Create a protected environment file
sudo nano /etc/obstacle-glasses.env
OPENAI_API_KEY=your_key_here
sudo chmod 600 /etc/obstacle-glasses.env
Keep the key private
Don’t put it in the script, a public repository, screenshots, or shared slides.
The system service reads this file on startup.

## Slide 8
SMART OBSTACLE GLASSES / SETUP
Configure automatic startup
RASPBERRY PI BUILD GUIDE • 08
The service example assumes username pi and this project folder:
/home/pi/obstacle-glasses/
Copy the service file to:
/etc/systemd/system/obstacle-glasses.service
Use the virtual environment interpreter in ExecStart:
/home/pi/obstacle-glasses/.venv/bin/python /home/pi/obstacle-glasses/test1.py
Change User= and paths if your Pi account or folder differs.

## Slide 9
SMART OBSTACLE GLASSES / SETUP
Enable and check the service
RASPBERRY PI BUILD GUIDE • 09
After installing the service file and environment file, run:
1
sudo systemctl daemon-reload
2
sudo systemctl enable --now obstacle-glasses.service
3
systemctl status obstacle-glasses.service
4
journalctl -u obstacle-glasses.service -f
The program starts on each boot and systemd restarts it if it exits with an error.

## Slide 10
SMART OBSTACLE GLASSES / SETUP
First run checklist
RASPBERRY PI BUILD GUIDE • 10
01
Boot
Service starts; distance alert runs in background.
02
Approach obstacle
Pulse spacing decreases inside the 5 ft alert zone.
03
Press then release
Camera captures; AI describes; speaker plays speech.
04
Troubleshoot
Read service logs; check camera, Wi-Fi, audio, API key, and wiring.
Use as a prototype; test in a safe familiar place and keep other obstacle-awareness methods available.